## Slide 1: EMG DESC Electrodes
Graphical Programming Exam Project

## Slide 2: Summary
General Characteristics
Aim of the Project
Work Pipeline
  0. Load of the Data + Selection of the Mode (Raw/Env)
  High Pass Filtering
  Full Wave Rectification
  Low Pass Filtering
  Normalisation
  Thresholding
Results

## Slide 3: General Characteristics
Acquire EMG Signals in 2 Different Modalities
  Raw Data (without any preprocessing)
  Enveloped (Filtered and Rectified)
Produce a Feedback stimulation through a Motor
Processed EMG
Feedback Sensation
Artefacts
Surface EMG
Amplifier
Anti-Aliasing FIlter
ADC
4. Norma-isation
3. Smoothing
2.
Full-wave Rectifier
1. Filtering
5. Thresholding
Processing Pipeline

## Slide 4: Aim of the Project
Create a Labview pipeline for the offline automatic process of DESC electrodes EMG Data
Compare the results of a simple threshold segmentation to extract the useful EMG (from Environmental and Motor Noises)
Environmental Noise
Motor Noise
Useful EMG

## Slide 5: 0. Load of the Data

## Slide 6: 0. Selection of the Mode

## Slide 7: 1. High Pass Filtering
2nd Order, zero phase, HP, Butterworth Filter

## Slide 8: 2. Full Wave Rectification
Vout = |Vin|

## Slide 9: 3. Low Pass Filtering
2nd Order, zero phase, LP, Butterworth Filter

## Slide 10: 4. Normalisation
Vout(k) = (Vin(k) – Vmin) / (Vmax - Vmin)

## Slide 11: 5. Thresholding

## Slide 12: Results
With the thresholding, the enveloped signal was correctly segmented.
While some motor artefacts were too prominent in the Raw signal to be filtered out.